## Slide 1: An introduction to Writing Transport SDN Applications (Hands-on)
Ricard Vilalta (CTTC/CERCA), Karthik Sethuraman (NEC Corporation)
OFC 2017 - SC449

## Slide 2: Short course Materials
VirtualBox VM image:
  http://tiny.cc/ofc-tapi-sc
Github repository:
  https://github.com/rvilalta/OFC_TAPI_SC

## Slide 3: Outline
13:30 – 13:35 : Welcome, agenda and motivation
13:35 – 14:15 : TAPI Concepts
  Context, Topology, Connectivity, etc
14:15 - 15:00 : TAPI SDK & Tooling Overview
  UML, YANG, SWAGGER, RI, Extensions/Specification
15:00 - 16:00 : Hands-on : Using TAPI
  Modelling: Create simple vendor-specific extensions in UML
  Tooling: Generate YANG & SWAGGER modules from UML
  Coding: Write logic & execute RI - Server & Client application in Python
16:00 - 16:30 : Coffee break
16:30 - 17:30 : Hands-On : Using ODL/ONOS with TAPI
  Introduction to ODL/ONOS northbound REST API, and how it might be used to establish T-API connectivity services

## Slide 4: Transport SDN - Motivation

## Slide 5: What we see in the market ?
A New Kind of Business Customer
A New Kind of Business Customer
Private and public cloud
Elastic compute and storage
Elastic
Compute & Storage
Requires an Elastic Network
A New Kind of Service Provider
SaaS, IaaS, PaaS
Elastic compute & storage
Multi-tenant
A New Network is Required
Hypergrowth - Mobile, Video, Cloud…
A New Kind
of Consumer
Living in the cloud
Streaming Downloads
Driving new network loads
Bandwidth-on-demand to match the compute/storage on-demand technology
Multi-tenant
Higher utilization, greater efficiency
Scalable and resilient
Faster service deployment

## Slide 6: Why is SDN different from traditional SDN Architectures?
OSS/BSS System
NMS/ EMS
NE
NE
NE
Traditional
Architecture
SDN Controller
Apps/ Orch
NE
NE
NE
SDN Architecture
  The difference is NOT:
  Standardized Management Interfaces
  Standardized Architecture
  Partly not the Open Interfaces
  Partly not even the use cases
  The difference is:
  A new way of thinking
  Application focused
  Application takes control over the service
  Open Source based development
  Simplification through Abstraction & Virtualization

## Slide 7: Why do we need SDN in Transport?
  Programmability:
  Programmable interfaces
  Applications focused architecture
  Abstraction & Virtualization
  Multi-Tenant capabilities
  Integration focused:
  Multi-layer
  Multi-vendor
  Innovation:
  Opens doors for new service models
  Service differentiation through new application
  Simplified Architectures:
  Integrated E2E / Multi-layer service creation
  Automatic reaction on errors or any changes
  Financial Benefits:
  Opex: efficient service setup
  Capex: fast ROI / hardware utilization
  New revenue opportunities
  Openness:
  Open Stanadsrds & Interfaces
  Open Source SW
Principles of SDN
What it Enables in Transport Network

## Slide 8: Keys to success

## Slide 9: 2014 OIF-ONF Transport SDN Interop Demo

## Slide 10: 2016 OIF-ONF Transport SDN Interop Demo Telefónica Lab
Traffgen
Traffgen
Optical Controller
Provisioning app
MD Controller/Orchestrator
Optical Controller
Optical Controller
Optical Controller
MD Controller/Orchestrator
Optical Controller

## Slide 11: ONF Transport API (TAPI) Overview

## Slide 12: Transport API: Simple Problem Statement….
Open
Standard
T-API
ONOS
ODL
Proprietary/ Legacy Systems
Network Orchestrator
APP
ONOS APIs
ODL APIs
Proprietary APIs

## Slide 13: Transport API Project Overview
Objective – realize a software-centric approach to standardization
  Purpose-specific API to facilitate SDN control of Transport networks
  Focus is on functional aspects of transport network control/mgmt
  Target is YANG & JSON API libraries
  Demonstrable code
Activity scoped based on use case contributions and discussions. Examples include
  Bandwidth on Demand
  E2E Connectivity Service
  Multi-layer Resource Optimization and Restoration
  Multi-Domain Topology and Monitoring
  Network Slicing and Virtualization
Topology Service
  Retrieve Topology, Node, Link & Edge-Point details (Across al layers)
Connectivity Service
  Retrieve & Request P2P, P2MP, MP2MP connectivity (Across all layers)
Path Computation Service
  Request for Computation & Optimization of paths
Virtual network Service
  Create, Update, Delete Virtual Network topologies
Notification Framework
  Subscription and filtering
  Autonomous mechanism
TAPI 2.0
  Protection, OAM, Alarm & TCAs
  Node Connectivity Constraints

## Slide 14: ONF Transport – API & Interfaces: Functional Architecture
Topology Service
Connectivity Service
Path Computation Service
Shared Network Information Context
Virtual Network Service
Notification Service
NE
Network Resource Groups
NE
NE
SDN Controller
NE
NE
SDN Controller
NE
NE
Application
Transport API
Transport API
SBIs (e.g. TL1, Openflow Optical, etc)

## Slide 15: TAPI Concepts Overview
All TAPI interaction between an API provider (e.g. SDN Controller) and an API Client (e.g. Application, Orchestrator or SDN Controller) occur within a shared “Context”
TAPI Context is defined by a set of ServiceEndPoints (and some policy)
  ServiceEndPoints enable requesting of TAPI Services (e.g. ConnectivityService) between them.
  With reference to ConnectivityServices, a ServiceEndPoint conceptually represents a pool of “potential” ConnectionEndPoints.
A TAPI provider may expose one or more abstract Topology within the shared Context
  These topologies may or may-not map 1-to-1 to a provider’s internal topology.
A Topology is expressed in terms of Nodes and Links between them.
  Links terminate on NodeEdgePoints, Nodes aggregate NodeEdgePoint
  NodeEdgePoint and ConnectionEndPoints have a server-client/mux-demux, etc relationship in terms of data-plane signal hierarchy
TAPI provider creates(provisions) one or more Connections in response to a successful ConnectivityService request between a set of 2 or more ServiceEndPoints
  ConnectionEndPoints encapsulate information related to a Connection at the ingress/egress points of every Node that the Connection traverses in a Topology
  Knowledge of Topology is needed to understand the Route of a Connection
  Route of a Connection is described as a list (series) of lower-level Connections

## Slide 16: TAPI Interface Overview
TAPI SDK 1.0 is an initial release that targets interfaces to key Transport SDN controller functions
Topology Service
  Retrieve Topology, Node, Link & Edge-Point details – (L0-L2) layers
Connectivity Service
  Retrieve & Request P2P, P2MP, MP2MP connectivity - (L0-L2) layers
Path Computation Service
  Request for Computation & Optimization of paths
Virtual Network Service
  Create, Update, Delete Virtual Network topologies
Notification Framework
  Subscription and filtering
  Autonomous mechanism

## Slide 17: T-API Shared Context
Shared Context – entire context for the T-API Provider & Client interaction
  Context for Topology, Connectivity, Path Computation, Virtual Network and Notification Service APIs
  Defined by set of Service-End-Points
  Includes one or more top-level Topologies within the shared context that are
    Either statically assigned by the Provider
    Or dynamically created by the Client using Virtual Network Service API
    Defined by a set of Nodes and Links
    A Node aggregates Node-Edge-Points, Link terminates on Node-Edge-Points
    A Node can encompass an internal Topology and be recursively decomposed into its lower-level Nodes and Links
  Provides scope for control (create/update/delete) of Connections (and its Connection-End-Points) using Connectivity Service APIs
  Utilizes one or more shared namespace
  Setup & requirements of shared context depends on offline negotiation/agreement between TAPI provider & its client
    Determines type and degree of abstraction that is provided
Must not be confused with API provider’s or client’s internal context

## Slide 18: Topology Service (Retrieval APIs only)
Get Topology Details
  Returns attributes of the Topology identified by the provided input Id .
  This includes references to lower-level Nodes & Links encompassed by the Topology
Get Node Details
  Returns attributes of the Node identified by the provided input Id .
  This includes references to Node-Edge-Points aggregated by the Node
  This also includes attributes representing the identification, naming, states and forwarding capabilities of the Node.
Get Link Details
  Returns attributes of the Link identified by the provided input Id.
  This includes references to Node-Edge-Points terminating the Link.
  This includes references to the Nodes associated by the Link.
Get Node-Edge-Point Details
  Returns attributes of the Node-Edge-Point identified by the provided input Id.
  This currently does NOT include reference to mapped/contained Service-End-Points or Connection-End-Points
    TAPI Service-End-Point/Connection-End-Point instead have references to the associated Node-Edge-Point
All of the APIs support a retrieve-scope Filter: Layer-Protocol List
  If set, API call will return output that is relevant to the specified Layer only

## Slide 19: Connectivity Service (Retrieval API)
Get Connectivity Service-End-Point List
  Returns list of ServiceEndPoints that can be used or being used in a connectivity Service request
  This also includes the attribute details for each ServiceEndPoint
Get Connectivity Service-End-Point Details
  Returns attributes of the ServiceEndPoint identified by the provided input Id.
Get Connectivity-Service List
  Returns list of Service entities that represent the connectivity requests that were received
  This also includes attribute details for each Service including
  Includes references to ServiceEndPoints terminating the Service
  Optionally includes references to any Connections realizing the Service
Get Connectivity-Service Details
  Returns attributes of the Service entity identified by the provided input Id, that represents a received connectivity request.
  This includes references to ServiceEndPoints terminating the Service.
  This optionally includes references to any Connections realizing the Service.
Get Connection Details
  Returns attributes of the Connection entity identified by the provided input Id.
  This includes references to ConnectionEndPoints terminating the Connection.
  This includes references to Paths in the underlying Topology.
  This includes reference to the Node containing this Connection.
Get Connection-End-Point Details
  Returns attributes of ConnectionEndPoint identified by the provided input Id.
  This includes reference to the NodeEdgePoint containing this ConnectionEndPoint.

## Slide 20: Connectivity Service (Request)
Related to creation of forwarding entities
  Intent-like – option allows the TAPI Provider to compute path and realize the service request
  Current focus is point-to-point
    Many initial uses, e.g., BoD, DC Interconnect
    Prototyped in 2014 Demonstration
  APIs flexible to support other types (p2mp, mp2mp) - Use case analysis planned in near future
Create Connectivity Service
  Service Endpoint List – each Endpoint is described by
    Name (TRI/URI/Proprietary string)
      TRI formats for ODU, ETH, MPLS-TP to be specified by the IA (implementation)
    Role (Symmetric, Root, Leaf) and Directionality (Input, Output, Bidirectional)
    Layer of the ServiceEndPoint if it supports multiple layers
  Connectivity Requirements
    Service Type (P2P, P2MP, MP) - required
    Capacity/Bandwidth – fixed or a range – required
    Service Layer (ETH, MPLS-TP, ODU, OCH)
    Service Level - a abstract value the meaning of which is mutually agreed – typically represents metrics such as - Class of service, priority, resiliency, availability
    Latency - integer value and unit - upper bound
    Cost - Vector of one or more metrics that would enable the provider to make a decision when implementing the Service
    Coroute-Inclusion or Diversity Exclusion - an include/exclude Service ID(s) –indicates that the requested service should be co-routed or diverse (not share resources) from specified service
    Include Path – indicates partial set of nodes and links to be used
    Exclude Path - indicates partial set of nodes and links to be avoided
    Start Time & End Time
  Output: Service ID and the created Connection

## Slide 21: Path Computation Service (Request)
Compute P2P Path
  The API client can request the API provider to compute a single path or a batch of paths with provided set of constraints
  The API provider should have topology information (including TE information) of the network in which the path computation is applied
  Inputs
    Service Endpoint List – same endpoints as the Connectivity API
    Routing (Connectivity) Constraints including
      Required Constraints such as Capacity
      Optional Constraints such as Layer, Latency, Cost, etc
    Objective function
  Output
    A list of Path options each of which is an ordered list of TE Links – either as strict hops (NodeEdgePoints) or loose hops (Nodes)
Optimize P2P Path
  Modify an existing path to optimize as per the objective function
  In addition to above, is provided Optimization Constraints as input

## Slide 22: Virtual Network Service (Request)
APIs to allow an API-Client to request creation, deletion, update of virtual network (client created) Topologies with its shared context
Create Virtual Network (VN) Topology
  Inputs
    Service Endpoint List – same endpoints as the Connectivity API
    Topology Constraints including
      Traffic matrix: A matrix to describe the traffic (e.g. bandwidth) between each pair of the client’s access points
      Optional Constraints such as Layer, Latency, Cost, etc
    Start Time & End Time
  Output
    Topology ID of the topology that has been created
The VN Topology can be retrieved using Topology Service API and is no different than the static Provider created topology
  API Client would use the Connectivity Service APIs to create Connections on-demand over the VN Topology

## Slide 23: TAPI Resource : Topology Constructs
(API) Context – defines the scope of control and naming that a particular T-API provider or its client application has with respect to the information exchanged over the interface.
  This Context is shared between the API provider and its client and determines the makeup of the network resource abstractions over which the API operates.
Topology – representation of the transparent topological-aspects of a Forwarding-Domain (FD)
  Topology describes the underlying topological network of Nodes and Links that enable the forwarding function provided by the FD.
Node – representation of the opaque forwarding-aspects of the Forwarding-Domain (FD)
  Node describes the edge ports of the FD (Node-Edge-Point) and the forwarding capabilities between those edge ports.
Link – representation of the effective adjacency between two or more associated Nodes in a Topology.
  Link is terminated by Node-Edge-Points of the associated Nodes. The Node-Edge-Points have a specific role with respect to the Link

## Slide 24: TAPI Resource: End-Point/Termination Constructs
Node-Edge-Point - represents the node-facing aspect of the edge-port functions for accessing the forwarding capabilities provided by the Node.
  Node-Edge-Point provides an encapsulation of addressing, mapping, termination, adaptation and OAM functions of one or more transport layers (including circuit and packet forms) performed at the entry/exit points of Node.
Service-End-Point - represents the outward-facing aspect of the edge-port functions for accessing the forwarding capabilities provided by Node.
  Service-End-Point provides a limited, simplified view of interest to external clients (e.g. client addressing, capacity, resource availability, etc), that enable the clients to make a connectivity service request without the need to understand the provider network internals.
  Service-End-Point have a mapping relationship (one-to-one, one-to-many, many-to-many) to Node-Edge-Points
Connection-End-Point - represents the ingress/egress port functions for accessing to the forwarding function provided by the Connection.
  Connection-End-Point have client-server relationship with Node-Edge-Points

## Slide 25: TAPI Resource : Forwarding Constructs
Connectivity Service - represents an “intent-like” request for connectivity between two or more Service-End-Points.
  Service is a container for connectivity request details and is distinct from Connection that realizes the request
  They refer to different aspects of information exchanged over T-API interface, but within provider they could be modeled by the same instance if there is one-to-one mapping.
Connection - represents an enabled (provisioned) potential for forwarding (including all circuit and packet forms) between two or more Node-Edge-Points of a Node.
  Connection is a container for provisioned connectivity that tracks the state of the allocated resources and is distinct from the connectivity Service request.
Path - represents the route of a Connection through the lower-level Nodes in the underlying Topology
  Path is described as a list of references to the lower-level Connections.

## Slide 26: TAPI Concepts & Example

## Slide 27: Simple Physical Network Example to illustrate T-API
PE3
PE1
PE2
P
CE4
CE3
CE5
CE – Customer Edge
PE – Provider Edge
P - Provider
CE1
CE2
CE6
Node Edge Point (Network Internal)
Service EndPoint
Node Edge Point (Network Edge)
UNI
UNI
UNI
A Network Provider (Blue) with two Customers (Red and Green)
All UNI interfaces are ETH (e.g. 10GE), I-NNI interfaces are OTU (e.g. 100G OTN)
All PE-NE are ODU/ETH capable, while P-NE is only ODU capable

## Slide 28: T-API Contexts for the Simple Network Example (based on ONF Architecture v1.1)
Resource Group - PE1
Resource Group - PE2
Resource Group - PE3
Resource Group - P
Other Admin Interfaces
Provider Internal Context
Server Context
PE1
Server Context
PE2
Server Context
PE3
Server Context
P
Shared Context
RED
Resource Group
TAPI
Shared Context
GREEN
Resource Group
TAPI
Shared Context
BLUE.Admin
Resource Group
TAPI
Application
RED
SDN Controller GREEEN
Resource Group
Resource Group
Admin APP
Blue
Client
Server
Client
Server
Provider SDN Controller
Orchestration / Virtualization

## Slide 29: Example Shared Contexts
Node Edge Point (NW Internal)
Service End Point
Node Edge Point (NW Edge)
Link
Mapping
Topology
Node
G1
G2
G3
Green Shared Context
R1
Red Shared Context
P
PE1
PE2
PE3
Blue Internal Context

## Slide 30: Recursive Topology Decomposition within a Shared Context
Node Edge Point (NW Internal)
Service End Point
Node Edge Point (NW Edge)
Link
Mapping
Topology
Node
R1
Red Shared Context
R1
Red Shared Context
R1.1
R1.2
R1.3

## Slide 31: Client1 (Red) Shared Context (empty Topology example)
Connection
Connectivity Service
Node Edge Point (Internal)
Service End Point
Node Edge Point (Edge)
Link
Transitional Link
Mapping
Topology
Node
Connection EndPoint
Connection
Shared Context
Shared Context defined by the set of ServiceEndPoints
No Topology exposed - Retrieving topology will return empty
ConnectivityService can be requested between ServiceEndPoints
  Client provides input ConnectivityConstraints – Capacity/BW is the only required input
Associated Connection representing network resources is created/returned to Client

## Slide 32: Client-1 (Red) Shared Context (Single Node Topology example)
ETH
Connection
Connectivity Service
Shared Context
Node Edge Point (Internal)
Service End Point
Node Edge Point (Edge)
Link
Transitional Link
Mapping
Topology
Node
Connection EndPoint
Connection
Single Node abstraction example
Node and its NodeEdgePoints provide some approximation of the network capabilities
ConnectivityService can be requested between ServiceEndPoints
Connections appear as cross-connections across node, no visibility of underlying route

## Slide 33: Client 2 (Green) Shared Context (Multi-Node Topology example)
PE1
PE3
PE2
ETH
Connection
Connectivity Service
Shared Context
Node Edge Point (Internal)
Service End Point
Node Edge Point (Edge)
Link
Transitional Link
Mapping
Topology
Node
Connection EndPoint
Connection
Multiple Nodes (PEs) Topology example
Node and its NodeEdgePoints provide reasonable information of their capabilities
ConnectivityService can be requested between ServiceEndPoints
Connection route can be traced over the exposed Topology

## Slide 34: Admin (Blue) Shared Context (example Multi-layer Topology)
34
PE1
PE3
P
PE2
PE1
PE3
PE2
ODU
ETH
Connectivity Service
Connection
Shared Context

## Slide 35: Client-1 (Green) Shared Context (Virtual Network Topology example)
ETH
VN Topology Service
PE1
PE3
PE2
Connectivity Service
Shared Context
Node Edge Point (Internal)
Service End Point
Node Edge Point (Edge)
Link
Transitional Link
Mapping
Topology
Node
Connection EndPoint
Connection
Client requests VN Topology between ServiceEndPoints within its Shared Context
Provider creates a Topology based on the input Topology constraints (e.g. traffic matrix)
Single Node or Multiple Node abstraction of Topology
Node and its NodeEdgePoints provide some approximation of the network capabilities
ConnectivityService can be requested between ServiceEndPoints

## Slide 36: TAPI Multi-domain Concepts & Example

## Slide 37: Multi-Domain Physical Network Example to illustrate T-API
D1-3
D1-1
D1-2
D1-4
R-1
R-3
G-1
G-3
3
4
Node Edge Point (Network Internal)
1
Service EndPoint
Node Edge Point (Network Edge)
UNI
NNI
UNI
3 Network domain (Blue) with two Customer domains (Red and Green)
All UNI interfaces are ETH (e.g. 10GE), NNI interfaces are OTU (e.g. 100G OTN)
All UNI boxes are ODU+ETH switch capable, while rest are only ODU switch capable
NNI
D2-3
D2-1
D2-2
5
6
Domain-1
Domain-2
1
2
D3-3
D3-1
D3-2
D3-4
R-2
R-4
G-2
G-4
10
9
UNI
UNI
11
12
7
8
Domain-3

## Slide 38: Reference Multi-domain Hierarchical Control Example
TAPI Context-1
TAPI Context-R
TAPI Context-G
Domain-1 Controller
Domain-2 Controller
Domain-3 Controller
Multi-Domain Controller
1.D1
2.D1
5.D1
6.D1
TAPI Context-2
5.D2
6.D2
7.D2
8.D2
TAPI Context-3
7.D3
8.D3
11.D3
12.D3
1.G
10.G
2.R
9.R
3.D1
4.D1
9.D3
10.D3
3.G
11.G
4.R
12.R
R-1
3
4
UNI
NNI
UNI
G-1
NNI
5
6
Domain-1
1
2
7
8
Domain-2
D1-4
D1-1
D1-2
D1-3
D2-1
G-3
R-3
R-2
10
9
UNI
G-2
11
12
D3-4
D3-1
D3-2
D3-3
G-4
R-4
D2-2
D2-3
Abstraction & Orchestration
Abstraction & Orchestration
Abstraction & Orchestration
Domain-3
UNI
Abstraction & Orchestration
Node Edge Point (Network Internal)
1
Service EndPoint
Node Edge Point (Network Edge)
3 Provider domains (Blue)
2 Customer domains (Red and Green)
All UNI interfaces are ETH (e.g. 10GE)
NNI interfaces are OTU (e.g. 100G OTN)
All UNI devices are ODU+ETH switch capable
Internal devicesare only ODU switch capable

## Slide 39: Domain-1 TAPI Context Topology
D1-o
D1-e
1.D1
2.D1
5.D1
6.D1
3.D1
4.D1
D1
This slide depicts the complete Topology exposed by domain-controller 1 to the multi-domain-controller*
It is assumed that the exposed TAPI-Context Topology is a 2 Node abstraction (1 per layer) of domain-controller ‘s internal Context
It is assumed that no Connectivity has been setup in the entire domain and this is the initial Topology view
TAPI Context-1
  *The multi-domain controller may have to invoke more than one retrieval API operation to get this view
D1-3
D1-1
D1-2
D1-4
R-1
R-3
G-1
G-3
3
4
UNI
UNI
Domain-1
1
2
Physical Box View (internal)
5
6
Node Edge Point (Internal)
Service End Point
Node Edge Point (Edge)
Link
Transitional Link
Mapping
Topology
Node
Connection EndPoint
Connection
Connectivity Service
NNI

## Slide 40: Domain-2 TAPI Context Topology
This slide depicts the complete Topology exposed by domain-controller 2 to the multi-domain-controller*
It is assumed that the exposed TAPI Context Topology is same as the domain-controller’s internal Context
It is assumed that no Connectivity has been setup in the entire domain and this is the initial Topology view
D2-3o
D2-2o
6.D2
5.D2
8.D2
7.D2
D2-1o
D2
TAPI Context-2
  *The multi-domain controller may have to invoke more than one retrieval API operation to get this view
D2-3
D2-1
D2-2
Physical Box View (internal)
Domain-2
5
6
7
8
Node Edge Point (Internal)
Service End Point
Node Edge Point (Edge)
Link
Transitional Link
Mapping
Topology
Node
Connection EndPoint
Connection
Connectivity Service
NNI
NNI

## Slide 41: Domain-3 TAPI Context Topology
D3-1o
D3-4o
D3-2o
11.D3
12.D3
9.D3
10.D3
D3-3o
D3-2e
D3-1e
7.D3
8.D3
D3
This slide depicts the complete Topology internal to the multi-domain-controller*
It is assumed that the exposed TAPI Context Topology is same as the domain-controller’s internal Context
It is assumed that no Connectivity has been setup in the entire domain and this is the initial Topology view
TAPI Context-3
  *The multi-domain controller may have to invoke more than one retrieval API operation to get this view
D3-3
D3-1
D3-2
D3-4
R-2
R-4
G-2
G-4
10
9
UNI
UNI
11
12
7
Domain-3
8
Physical Box View (internal)
Node Edge Point (Internal)
Service End Point
Node Edge Point (Edge)
Link
Transitional Link
Mapping
Topology
Node
Connection EndPoint
Connection
Connectivity Service
NNI

## Slide 42: Domain-3 TAPI Context Hierarchical Topology (2-Level)
D3-1o
D3-4o
D3-2o
11.D3
12.D3
9.D3
10.D3
D3-3o
D3-2e
D3-1e
D3o
D3e
7.D3
8.D3
D3
This slide depicts complete Topology exposed to multi domain-controller as 2-Level hierarchy*
  It is assumed that the exposed TAPI Context top-level Topology is an 2 Node abstraction of domain-controller‘s internal Context
  This view is constructed by recursively traversing/expanding the internal Topology of top-level Nodes
It is assumed that no Connectivity has been setup in the entire domain and this is the initial Topology view
TAPI Context-3
  *The multi-domain controller may have to invoke more than one retrieval API operation to get this view
D3-3
D3-1
D3-2
D3-4
R-2
R-4
G-2
G-4
10
9
UNI
UNI
11
12
7
Domain-3
8
Physical Box View (internal)
D3e
D3o
Node Edge Point (Internal)
Service End Point
Node Edge Point (Edge)
Link
Transitional Link
Mapping
Topology
Node
Connection EndPoint
Connection
Connectivity Service
NNI

## Slide 43: MD Controller Local Resource Pool (Internal)
D1-o
D1-e
D3-1o
D3-4o
D3-2o
11.D3
12.D3
10.D3
9.D3
D3-3o
D3-2e
D3-1e
7.D3
8.D3
D2-3o
D2-2o
6.D2
5.D2
8.D2
7.D2
D2-1o
D2
D3
1.D1
2.D1
5.D1
6.D1
3.D1
4.D1
D1
MD Controller Internal View (not exposed)
This slide depicts the complete Topology internal to the multi-domain-controller in terms of TAPI-like constructs*
  This view is not exposed to the applications over TAPI.
  The abstraction mapping is maintained internally by the MD domain controller
  The MD controller is responsible for matching-up and mapping the service-end-points of different domains
It is assumed that no Connectivity has been setup in the entire domain and this is the initial internal Topology view
* An controller internal model may not be based on TAPI
1.G
2.R
3.G
4.R
11.G
12.R
10.G
9.R

## Slide 44: Green TAPI Context Topology (single-layer, single Node topology example)
This slide depicts the complete Topology exposed by the multi-domain-controller to the Green application
It is assumed that exposed TAPI-Context Topology is a single Node abstraction of multi-domain-controller ‘s internal Context
It is assumed that this is an ETH layer Topology
  The LayerProtocol of NodeEdgePoints contain attributes specified by the Ethernet extension schema
It is also possible that no layer information is exposed and layer specific information is implicitly known to client and provider
It is assumed that no Connectivity has been setup in the entire domain and this is the initial Topology view
  *The application may have to invoke more than one retrieval API operation to get this view
G1.e
1.G
3.G
G
Green TAPI Context
11.G
10.G
Node Edge Point (Internal)
Service End Point
Node Edge Point (Edge)
Link
Transitional Link
Mapping
Topology
Node
Connection EndPoint
Connection
Connectivity Service

## Slide 45: Green TAPI Context Topology (single layer, edge-Node topology example)
R1.e
This slide depicts an alternate Topology exposed by the multi-domain-controller to the Green application
It is assumed that exposed TAPI-Context Topology is an edge-Node abstraction of multi-domain-controller ‘s internal Context
It is assumed that this is an ETH layer Topology
  The LayerProtocol of NodeEdgePoints contain attributes specified by the Ethernet extension schema
It is assumed that no Connectivity has been setup in the entire domain and this is the initial Topology view
  The ETH layer Links are an abstraction of the potential connectivity at this layer
  TAPI Capacity pac is used to represent all the potential, provisioned and available capacity information
  *The application may have to invoke more than one retrieval API operation to get this view
1.G
3.G
G
Green TAPI Context
11.G
10.G
R3.e
R2.e
Node Edge Point (Internal)
Service End Point
Node Edge Point (Edge)
Link
Transitional Link
Mapping
Topology
Node
Connection EndPoint
Connection
Connectivity Service

## Slide 46: Red TAPI Context Topology (multi-layer example)
R3.o
R1.o
R1.e
This slide depicts a multilayer Topology exposed by the multi-domain-controller to the Red application
It is assumed that exposed TAPI-Context Topology is per-layer-Node abstraction of multi-domain-controller’s internal Context
It is assumed that this is an ETH + ODU layer Topology
It is assumed that no Connectivity has been setup in the entire domain and this is the initial Topology view
  Initially there no Links in the ETH layer
  The ODU layer Links are an abstraction of the potential connectivity at this layer
  *The application may have to invoke more than one retrieval API operation to get this view
2.R
4.R
R
Red TAPI Context
12.R
9.R
R3.e
R2.o
Node Edge Point (Internal)
Service End Point
Node Edge Point (Edge)
Link
Transitional Link
Mapping
Topology
Node
Connection EndPoint
Connection
Connectivity Service

## Slide 47: Red TAPI Context Topology (multi-layer example)
R3.o
R2.o
R1.o
R1.e
This slide depicts an alternate Topology exposed by the multi-domain-controller to the Red application
It is assumed that exposed TAPI-Context Topology is an edge-Node abstraction of multi-domain-controller ‘s internal Context
It is assumed that this is an ETH + ODU layer Topology
It is assumed that no Connectivity has been setup in the entire domain and this is the initial Topology view
  Initially there no Links in the ETH layer
  The ODU layer Links are an abstraction of the potential connectivity at this layer
  *The application may have to invoke more than one retrieval API operation to get this view
2.R
4.R
R
Red TAPI Context
12.R
9.R
R3.e
R2.e
Node Edge Point (Internal)
Service End Point
Node Edge Point (Edge)
Link
Transitional Link
Mapping
Topology
Node
Connection EndPoint
Connection
Connectivity Service

## Slide 48: Service Example 10G EPL
Node Edge Point (Network Internal)
1
Service EndPoint
Node Edge Point (Network Edge)
TAPI Context-1
TAPI Context-R
TAPI Context-G
Domain-1 Controller
Domain-2 Controller
Domain-3 Controller
Multi-Domain Controller
1.D1
2.D1
5.D1
6.D1
TAPI Context-2
5.D2
6.D2
7.D2
8.D2
TAPI Context-3
7.D3
8.D3
11.D3
12.D3
1.G
10.G
2.R
9.R
3.D1
4.D1
9.D3
10.D3
3.G
11.G
4.R
12.R
D1-3
D1-1
D1-2
D1-4
R-1
R-3
G-1
G-3
3
4
UNI
NNI
UNI
NNI
D2-3
D2-1
D2-2
5
6
Domain-1
1
2
D3-3
D3-1
D3-2
D3-4
R-2
R-4
G-2
G-4
10
9
UNI
UNI
11
12
7
8
Domain-3
Domain-2
1
2
3
4
5
13
6
8
7
9
11
10
12

## Slide 49: 10G EPL Service Setup Sequence
Green-app requests 10G EPL ConnectivityService between SEPs (1.G, 11.G)
MD-controller computes & provisions E2E connectivity within its internal topology
MD-controller requests 10G ConnectivityService between SEPs (1.D1, 5.D1)
  Domain1-controller computes & provisions ODU+ETH Connections in its domain
  Domain1-controller returns provisioned Connections in terms of Context-1 topology
MD-controller requests 10G ConnectivityService between SEPs (5.D2, 7.D2)
  Domain2-controller computes & provisions ODU Connections in its domain
  Domain2-controller returns provisioned Connections in terms of Context-2 topology
MD-controller requests 10G ConnectivityService between SEPs (7.D3, 11.D3)
  Domain3-controller computes & provisions ODU+ETH Connections in its domain
  Domain3-controller returns provisioned Connections in terms of Context-3 topology
MD Controller updates its internal Topology and resource pool capacity/usage metrics
MD-controller returns provisioned Connections in terms of Context-G topology
  MD-controller updates capacity/usage metrics in Context-G topology
1
2
3
4
5
6
7
8
9
10
11
12
13
parallel requests

## Slide 50: 10G EPL Service setup: Green Context
R1.e
  *The application may have to invoke more than one retrieval API operation to get this view
3.G
G
Green TAPI Context
10.G
R3.e
R2.e
Node Edge Point (Internal)
Service End Point
Node Edge Point (Edge)
Link
Transitional Link
Mapping
Topology
Node
Connection EndPoint
Connection
Connectivity Service
11.G
1.G
1
13

## Slide 51: 10G EPL Service setup: MD Controller Internal view
D1-e
D1-o
D3-1o
D3-4o
D3-2o
11.D3
12.D3
10.D3
9.D3
D3-3o
D3-2e
D3-1e
7.D3
8.D3
D2-3o
D2-2o
6.D2
5.D2
8.D2
7.D2
D2-1o
D2
D3
2.D1
5.D1
6.D1
3.D1
4.D1
D1
MD Controller Internal View (not exposed)
* An controller internal model may not be based on TAPI
2.R
3.G
4.R
12.R
10.G
9.R
1.G
11.G
1.D1
3
6
8
12
9
2
11
11
12
5
5

## Slide 52: 10G EPL Service setup: DC1/Context1 view
D1-o
D1-e
2.D1
6.D1
3.D1
4.D1
D1
TAPI Context-1
  *The multi-domain controller may have to invoke more than one retrieval API operation to get this view
D1-3
D1-1
D1-2
D1-4
R-1
R-3
G-1
G-3
3
4
UNI
UNI
Domain-1
1
2
Physical Box View (internal)
5
6
Node Edge Point (Internal)
Service End Point
Node Edge Point (Edge)
Link
Transitional Link
Mapping
Topology
Node
Connection EndPoint
Connection
Connectivity Service
NNI
3
5.D1
1.D1
4
5
5

## Slide 53: 10G EPL Service setup: DC2/Context2 view
D2-3o
D2-2o
6.D2
5.D2
8.D2
7.D2
D2-1o
D2
TAPI Context-2
  *The multi-domain controller may have to invoke more than one retrieval API operation to get this view
D2-3
D2-1
D2-2
Physical Box View (internal)
Domain-2
5
6
7
8
Node Edge Point (Internal)
Service End Point
Node Edge Point (Edge)
Link
Transitional Link
Mapping
Topology
Node
Connection EndPoint
Connection
Connectivity Service
NNI
NNI
6
8
7

## Slide 54: 10G EPL Service setup: DC3/Context3 view
D3-1o
D3-4o
D3-2o
11.D3
12.D3
9.D3
10.D3
D3-3o
D3-2e
D3-1e
7.D3
8.D3
D3
TAPI Context-3
  *The multi-domain controller may have to invoke more than one retrieval API operation to get this view
D3-3
D3-1
D3-2
D3-4
R-2
R-4
G-2
G-4
10
9
UNI
UNI
11
12
7
Domain-3
8
Physical Box View (internal)
Node Edge Point (Internal)
Service End Point
Node Edge Point (Edge)
Link
Transitional Link
Mapping
Topology
Node
Connection EndPoint
Connection
Connectivity Service
NNI
9
11
11
10

## Slide 55: TAPI SDK & Tooling Overview

## Slide 56: Key Features of TAPI SDK
Technology-agnostic API Framework
  Standardizes a single core technology-agnostic specification that abstracts common transport network functions
Modular & Extensible
  Functional features are packaged into small self-contained largely-independent modules
  TAPI Core Spec is designed to be fully extensible
    Extensions can be Technology, SDO, Operator or Vendor specific
Industry-wide Interoperability Objective – developed within
  Open Source SDN SNOWMASS project under Apache 2 license
SDK components generated using tools for agile prototyping
  YANG schema generated from UML using guidelines developed in an multi-SDO initiative (IISOMI)
  Swagger/JSON APIs generated from YANG following RESTConf specification

## Slide 57: TAPI – ONF and OSSDN Project Dependencies
TAPI FRS
Use cases & Requirements
TAPI UML Information Model
TAPI YANG
Data Schema
SWAGGER/REST APIs
TAPI Platform Abstraction Layer & Framework
ONF Core Information Model
ONF Technology Specification Models
UML-YANG
Generation Tool
YANG-SWAGGER Generation Tool
SNOWMASS TAPI SDK
ENGLEWOOD
EAGLE Modeling Tools
Open Model Profile
Code
OTN
(ITU-T G.874.1)
ETH
(ITU-T G.8052)
MPLS-TP
(ITU-T G.8152)
Python Reference Implementation
Python Stub Generation Tool
Optical Transport
MEF
Open CS Implementations
Packet WAN
Multi-carrier
T-SDN Interop
Implementation Agreements
OIF
Interop Implementations
NRM
MEF Models
NRP
ONF IMP
ONF OTWG
ITU-T SG15

## Slide 58: OpenSourceSDN.org
Public portal
  Not just ONF members
  Licensing, governance, Git repository, groups, collaboration
  Complementary to, collaborating with ONOS, ODL, OCP, OPNFV, OpenStack, O3…
Project EAGLE: OpenSourceSDN repository for the IISOMI (Informal Inter-SDO Open Model Initiative). Includes..
  OpenModelProfile and InterfaceModelProfile
    UML profiles used in TAPI and code generation tools
  Open source code to auto-generate YANG model code from the papyrus UML models
  Also includes code to generate Swagger/JSON schema from the YANG models as well as Pythin code stubs
Project SNOWMASS: OpenSourceSDN Repository for the ONF Transport API Project (TAPI) SDK. Includes
  TAPI Information Model (UML)
  TAPI YANG Data Schema auto-generated using OSSDN EAGLE project tools
  TAPI Swagger/JSON API specifications also using OSSDN EAGLE tools
  TAPI Reference Implementation in Python
  Supporting documentation
  Allows vendors to incorporate easily into their models and products.

## Slide 59: TAPI SDK: Organization and Modularity
ONF Transport API Functional Requirements – TR-527, June 2016
  ONF Open Transport WG Project
  Input to the TAPI SDK
Software-wise, TAPI SDK 1.0.0 is packaged as 4 eclipse sub-projects
  Papyrus-UML Information Model
    A pruned/refactored version of ONF Core IM
    Is a technology-agnostic generic framework + technology specific extensions (OTN, ETH)
  YANG Data Schema
    auto-generated from UML using OSSDN Eagle Tools
  Swagger-JSON RESTConf API
    auto-generated from YANG using OSSDN Eagle tools
  Reference Implementation (RI) in Python
Feature-wise, TAPI SDK is organized as a module-set of {UML-Model, YANG-Module, Swagger-API} per TAPI functional interface

## Slide 60: TAPI Projects & Models/Modules

## Slide 61: Papyrus UML
Eclipse Modeling Tools
Download Package
YANG IDE
JSON Editor Swagger

## Slide 62: Outline of Papyrus Perspective

## Slide 63: Constructing TAPI Modeling Environment

## Slide 64: TAPI Resource Dependencies
OpenModel_CommonDataTypes Repository*
OpenModel_StyleSheets Repository*
OpenModel_Profile Repository
OpenModel_CoreModel Repository
TAPI Repository
* not yet created
cloned

## Slide 65: GIT Workflow
My Remote Repository
Staging
EAGLE Open Source Remote Repository
Local Repository
Local Working Directory
clone
administrator
OpenModel Profile
OpenModel Profile
1
2
6
7
5
fork
0
remote on GitHub
local on my PC
4
create remote
fetch remote
merge
checkout branch
3
automatically
push
user

## Slide 66: YANG
YANG has... A reasonable self-contained specification
A focus on readers and reviewers
  Text-based
    Email, patch, and RFC friendly
Limited Scope, but extensible
Ability to model config data, state data, RPCs, and notifications
Experience gained by existing implementations
  Design is based on four proprietary modeling languages
Support for YANG
Running code (multiple implementations)
People outside the YANG team using it in other WGs in the IETF
Backing of several NETCONF implementers
Growing group of fans and admirers

## Slide 67: Easy to read, easy to learn
container system {
leaf host-name {
type inet:host;
description "Name of this host";
}
container services {
container ssh {
presence "Enables SSH";
description "SSH service specific configuration";
// more leafs, containers and stuff here...
}
}
}
<system>
<host-name>fred</host-name>
<services>
<ssh/>
</services>
</system>

## Slide 68: YANG module contents

## Slide 69: RESTCONF
RESTCONF
  Almost RFC
  RESTful protocol to access YANG defined data
  Representational State Transfer, i.e. server maintains no session state
  URIs reflect data hierarchy in a Netconf datastore
  HTTP as transport
  Data encaded with either XML or JSON
  Operations :

## Slide 70: RESTCONF HTTP tree
RESTCONF is a REST-like protocol that provides a HTTP-based API to access the data, modeled by YANG. The REST-like operations are used to access the hierarchical data within a datastore. The information modeled in YANG is structured in the following tree:
  /restconf/data : “Data (configuration/operational) accessible from the client but not editable”
  /restconf/modules : “Set of YANG models supported by the RESTCONF server”
  /restconf/operations : “Set of operations (YANG-defined RPCs) supported by the server”
  /restconf/streams: “Set of notifications supported by the server”

## Slide 71: YANG Mapping to JSON
JSON is a popular compact and easy to parse data format used by many REST APIs
Subset of YANG compatible XML documents can be translated to JSON text
Translation driven by YANG data model (must be known in advance)
YANG datatype information is used to translate leaf values to the most appropriate JSON representation
Slightly more compact (irrelevant with compression)
Increased human readability (less noise)

## Slide 72: YANG mapping to JSON vs XML

## Slide 73: Project EAGLE Uml2Yang
Objective
  Translates a UML (Unified Modeling Language) model to a YANG model defined in RFC6020
Scope
  Work with swagger tool to generate RESTful/RESTconf APIs
  Fed to controllers, Apps for interface generation
UML Model
YANG Model
UML to YANG Mapping Gdls
IETF RFC 6020
ONF TR-514

## Slide 74: UML to YANG Tool
Object
Classes
owned
Attributes
Associations
module
node
leaf
leaf-list
type
rpc
YANG Tool
UML model
YANG model
OpenModelProfile

## Slide 75: Validate/View YANG files
Eclipse xored IDE: RFC 6020 validation, GUI view
pyang: RFC 6020/6087 validation, command line
YANG validator: RFC 6020/6087 validation, online tool

## Slide 76: T-API Swagger specifications
The T-API Swagger specifications provide a mapping from the Yang data schema into JSON Swagger, which can then be used to generate Python and Java code for implementation of the API in RestConf.

## Slide 77: YANG data models
YANG is a modeling language designed to create data models for the NETCONF protocol and more recently to RESTCONF. YANG is capable to define configuration and operational state data, remote procedure calls (RPCs) and Notifications.
YANG includes description of:
  Config
  State
  RPCs
  Notifications

## Slide 78: RESTconf
RESTCONF is a REST-like protocol that provides a HTTP-based API to access the data, modeled by YANG. The REST-like operations are used to access the hierarchical data within a data store. The information modeled in YANG is structured in the following tree:
  /restconf/config : “Data (configuration/operational) accessible from the client but not editable”
  /restconf/modules : “Set of YANG models supported by the RESTCONF server”
  /restconf/operations : “Set of operations (YANG-defined RPCs) supported by the server”
  /restconf/streams: “Set of notifications supported by the server”. They are implemented in a websocket
With YANGs + RESTconf 
  We have the complete Transport REST NBI

## Slide 79: T-API Swagger: Documentation
Swagger is a project used to describe and document RESTful APIs.
Swagger 2.0 specification:
http://swagger.io/specification/

## Slide 80: T-API Swagger: From YANG to Swagger Specs
Project Eagle YangJsonTools
https://github.com/OpenNetworkingFoundation/EAGLE-Open-Model-Profile-and-Tools/tree/YangJsonTools
Includes a plugin for Pyang
https://github.com/mbj4668/pyang
Pyang is a YANG validator, transformator and code generator, written in python. It can be used to validate YANG modules for correctness, to transform YANG modules into other formats, and to generate code from the modules.
The project EAGLE YangJsonTools plugin processes the YANG files and describes the associated RESTconf interface using Swagger REST definitions.

## Slide 81: T-API Swagger: Editing Swagger Specs
Using Eclipse JSON editor
  Described in T-API Developer Guide
Using Swagger on-line editor
  http://editor.swagger.io/

## Slide 82: T-API Swagger: Understanding Swagger specs
Paths
  Each path may include CRUD (POST, GET, PUT, DELETE) if config
  Only GET is allow for State data
  Each CRUD includes the following details:
    Summary
    Parameters (in path or in body)
    Responses
    Produces/consumes

## Slide 83: T-API Swagger: Understanding Swagger specs
Definitions
  They allow inheritance (allOf)
  Items are described in properties
  Other descriptions might be referenced (e.g., connectivityService)

## Slide 84: Creating a T-API Reference Implementation
Project EAGLE JsonCodeTools
https://github.com/OpenNetworkingFoundation/EAGLE-Open-Model-Profile-and-Tools/tree/JsonCodeTools
Server Generator for Python
Python code that uses Swagger json outputs from YangJsonTools to generate a RESTful and websocket server and the defined swagger objects, paths and notifications.
SWAGGER files
Project EAGLE JsonCodeTools
T-API Reference Implementation

## Slide 85: TAPI Reference Implementation

## Slide 86: T-API RI: Reference Network
Described in: https://github.com/OpenNetworkingFoundation/Snowmass-ONFOpenTransport/blob/develop/TAPI_RI/server_backend_state.json

## Slide 87: T-API RI: Status load
In order to load this scenario in T-API RI, please use the following REST call:
curl -X POST -H "Content-Type: application/json" http://127.0.0.1:8080/backend/load_state/
Response: 200 Loaded State

## Slide 88: T-API RI: Basic commands I
GET topologies
curl -X GET -H "Content-Type: application/json" http://127.0.0.1:8080/restconf/config/Context/_topology/
Response:
{
"itemlist": [
"http://127.0.0.1:8080/restconf/config/Context/_topology/top0"
]
}

## Slide 89: T-API RI: Basic commands II
GET topology top0
curl -X GET -H "Content-Type: application/json" http://127.0.0.1:8080/restconf/config/Context/_topology/top0/
Response:
{
“_node” : [ … ],
“_link” : [ …],
“uuid” : “top0”
}

## Slide 90: T-API RI: Basic commands III
GET ServiceEndPoints
curl -X GET -H "Content-Type: application/json" http://127.0.0.1:8080/restconf/config/Context/_serviceEndPoint/
Response:
{
"itemlist": [
"http://127.0.0.1:8080/restconf/config/Context/_serviceEndPoint/se1",
"http://127.0.0.1:8080/restconf/config/Context/_serviceEndPoint/se2"
]
}

## Slide 91: T-API RI: Connectivity Service workflow

## Slide 92: T-API RI: Establish Connectivity Service
curl -X POST -H "Content-Type: application/json" http://127.0.0.1:8080/restconf/config/Context/_connectivityService/cs1/ -d‘
{"uuid":"cs1",
"_connConstraint":{
"serviceType":"POINT_TO_POINT_CONNECTIVITY", "serviceLayer":["OCH"] }, "_servicePort":[
{ "localId":"sp1", “serviceLayer":"OCH" , "direction":"BIDIRECTIONAL", "role":"SYMMETRIC", "_serviceEndPoint":http://127.0.0.1:8080/restconf/config/Context/_serviceEndPoint/se1
},
{ "localId":"sp2", "serviceLayer":"OCH" , "direction":"BIDIRECTIONAL", "role":"SYMMETRIC", "_serviceEndPoint":http://127.0.0.1:8080/restconf/config/Context/_serviceEndPoint/se2
} ]
}'

## Slide 93: T-API RI: Notifications
Notifications will be provided with Websockets. T-API reference implementation provides an example of a client accessing the websocket:
http://localhost:8182/restconf/streams/NotificationService

## Slide 94: T-API App
Objective:
  Retrieve Network Topology using T-API
Steps:
  Run TAPI-RI
  Load topological information:
  curl -X POST -H "Content-Type: application/json" http://127.0.0.1:8080/backend/load_state/
  Start coding using the following libraries:
    NetworkX
    Requests
    Json

## Slide 95: ODL/ONOS northbound REST API

## Slide 96: OpenDayLight NBI

## Slide 97: OpenDayLight NBI

## Slide 98: OpenDayLight NBI
sudo mn --topo linear,3 --mac --controller=remote,ip=127.0.0.1,port=6633 --switch ovs,protocols=OpenFlow13

## Slide 99: Setup ODL
curl -X PUT -H"Content-Type: application/json" -u admin:admin http://localhost:8181/restconf/config/l2switch-config:l2switch-config -d'{"l2switch-config": {"is-learning-only-mode": "true","is-install-dropall-flow": "true"}}‘
curl -X PUT -H"Content-Type: application/json" http://localhost:8181/restconf/config/arp-handler-config:arp-handler-config -u admin:admin -d'{"arp-handler-config": {"is-proactive-flood-mode": "false"}}‘

## Slide 100: ONOS architecture

## Slide 101: ONOS NBI
~/onos-1.7.1/apache-karaf-3.0.5/bin$ ./karaf
app activate org.onosproject.openflow

## Slide 102: Integrating with TAPI_RI
Topology
funcs_TapiTopology/context_TopologyUuidImpl.py
Connectivity
funcs_TapiConnectivity/context_ConnectivityserviceImpl.py

## Slide 103: Conclusion

## Slide 104: TAPI Next Steps – 2.0
ONF Transport API 2.0 focus items
  Node Configuration – functional aspects
    Includes Port/NodeEdgePoint configuration
    Termination functions, etc
    Forwarding, Processing
  Protection
    Multi-layer, Multi-Domain
    Based on focus use cases under discussion
  OAM/Monitoring
    Consistent Multi-layer abstraction and model – L0-L2
  Alarms/TCAs/Counters
  Multi-Point, Multi-Layer, Multi-Domain use case enhancements
  Virtual Transport Network enhancements
  Multi-Technology
    Microwave
    Ethernet

## Slide 105: Standards vs Open Source

## Slide 106: Transport SDN Benefits and Challenges

## Slide 107: References
ONF SDN Architecture 1.1 - https://www.opennetworking.org/images/stories/downloads/sdn-resources/technical-reports/TR-521_SDN_Architecture_issue_1.1.pdf
TAPI Functional Requirements 1.0 - https://www.opennetworking.org/images/stories/downloads/sdn-resources/technical-reports/TR-527_TAPI_Functional_Requirements.pdf
TAPI SDK (SNOWMASS) - https://github.com/OpenNetworkingFoundation/Snowmass-ONFOpenTransport
UML Tools (EAGLE) - https://github.com/OpenNetworkingFoundation/EAGLE-Open-Model-Profile-and-Tools
TAPI 1.0 SDK Overview ONF MWD, Sept 7, 2016 https://github.com/OpenNetworkingFoundation/Snowmass-ONFOpenTransport/raw/develop/DOCS/presentations/onf2016.307_TAPI_SDK.01.pptx
OFC 2017: OIF Interop – The Key to Unlocking the Benefits of SDN, Tuesday, 21 March; 15:00 - 16:00.
OFC 2017: ONF Session – The path Forward, Thursday, 23 March, 12:00 - 13:30
Victor Lopez, et al., Transport API: A Solution for SDN in Carriers Networks, ECOC 2016; 42nd European Conference on Optical Communication.

## Slide 108: Thank you! Questions?
ricard.vilalta@cttc.es
karthik.sethuraman@necam.com