## Slide 1: T-API Multi-layer Multi-domain Topology & Connectivity Example *
Karthik Sethuraman (NEC)
Sept 6, 2016
* animated slides

## Slide 2: TAPI Concepts Overview
All TAPI interaction between an API provider (e.g. SDN Controller) and an API Client (e.g. Application, Orchestrator or another SDN Controller) occur within a shared “Context”
TAPI Context is defined by a set of ServiceEndPoints (and some policy)
  ServiceEndPoints enable request of TAPI Services (e.g. ConnectivityService) between them.
  With reference to ConnectivityServices, a ServiceEndPoint conceptually represents a pool of “potential” ConnectionEndPoints.
TAPI provider creates(provisions) one or more Connections in response to a successful ConnectivityService request
  ConnectionEndPoints encapsulate information related to a Connection at the ingress/egress points of every Node that the Connection traverses in a Topology
  Knowledge of Topology is needed to understand the Route of a Connection
  Route of a Connection is described as a list (series) of lower-level Connections
A TAPI provider may expose one or more abstract Topology within the shared Context
  These topologies may or may-not map 1-to-1 to a provider’s internal topology.
A Topology is expressed in terms of Nodes and Links between them.
  Links terminate on NodeEdgePoints, Nodes aggregate NodeEdgePoint
  NodeEdgePoint and ConnectionEndPoints have a server-client/mux-demux, etc relationship in terms of data-plane signal hierarchy

## Slide 3: Multi-Domain Physical Network Example to illustrate T-API
D1-3
D1-1
D1-2
D1-4
R-1
R-3
G-1
G-3
3
4
Node Edge Point (Network Internal)
1
Service EndPoint
Node Edge Point (Network Edge)
UNI
NNI
UNI
3 Network domain (Blue) with two Customer domains (Red and Green)
All UNI interfaces are ETH (e.g. 10GE), NNI interfaces are OTU (e.g. 100G OTN)
All UNI boxes are ODU+ETH switch capable, while rest are only ODU switch capable
NNI
D2-3
D2-1
D2-2
5
6
Domain-1
Domain-2
1
2
D3-3
D3-1
D3-2
D3-4
R-2
R-4
G-2
G-4
10
9
UNI
UNI
11
12
7
8
Domain-3

## Slide 4: Reference Multi-domain Hierarchical Control Example
TAPI Context-1
TAPI Context-R
TAPI Context-G
Domain-1 Controller
Domain-2 Controller
Domain-3 Controller
Multi-Domain Controller
1.D1
2.D1
5.D1
6.D1
TAPI Context-2
5.D2
6.D2
7.D2
8.D2
TAPI Context-3
7.D3
8.D3
11.D3
12.D3
1.G
10.G
2.R
9.R
3.D1
4.D1
9.D3
10.D3
3.G
11.G
4.R
12.R
R-1
3
4
UNI
NNI
UNI
G-1
NNI
5
6
Domain-1
1
2
7
8
Domain-2
D1-4
D1-1
D1-2
D1-3
D2-1
G-3
R-3
R-2
10
9
UNI
G-2
11
12
D3-4
D3-1
D3-2
D3-3
G-4
R-4
D2-2
D2-3
Abstraction & Orchestration
Abstraction & Orchestration
Abstraction & Orchestration
Domain-3
UNI
Abstraction & Orchestration
Node Edge Point (Network Internal)
1
Service EndPoint
Node Edge Point (Network Edge)
3 Provider domains (Blue)
2 Customer domains (Red and Green)
All UNI interfaces are ETH (e.g. 10GE)
NNI interfaces are OTU (e.g. 100G OTN)
All UNI devices are ODU+ETH switch capable
Internal devicesare only ODU switch capable

## Slide 5: Domain-1 TAPI Context Topology
D1-o
D1-e
1.D1
2.D1
5.D1
6.D1
3.D1
4.D1
D1
This slide depicts the complete Topology exposed by domain-controller 1 to the multi-domain-controller*
It is assumed that the exposed TAPI-Context Topology is a 2 Node abstraction (1 per layer) of domain-controller ‘s internal Context
It is assumed that no Connectivity has been setup in the entire domain and this is the initial Topology view
TAPI Context-1
  *The multi-domain controller may have to invoke more than one retrieval API operation to get this view
D1-3
D1-1
D1-2
D1-4
R-1
R-3
G-1
G-3
3
4
UNI
UNI
Domain-1
1
2
Physical Box View (internal)
5
6
Node Edge Point (Internal)
Service End Point
Node Edge Point (Edge)
Link
Transitional Link
Mapping
Topology
Node
Connection EndPoint
Connection
Connectivity Service
NNI

## Slide 6: Domain-2 TAPI Context Topology
This slide depicts the complete Topology exposed by domain-controller 2 to the multi-domain-controller*
It is assumed that the exposed TAPI Context Topology is same as the domain-controller’s internal Context
It is assumed that no Connectivity has been setup in the entire domain and this is the initial Topology view
D2-3o
D2-2o
6.D2
5.D2
8.D2
7.D2
D2-1o
D2
TAPI Context-2
  *The multi-domain controller may have to invoke more than one retrieval API operation to get this view
D2-3
D2-1
D2-2
Physical Box View (internal)
Domain-2
5
6
7
8
Node Edge Point (Internal)
Service End Point
Node Edge Point (Edge)
Link
Transitional Link
Mapping
Topology
Node
Connection EndPoint
Connection
Connectivity Service
NNI
NNI

## Slide 7: Domain-3 TAPI Context Topology
D3-1o
D3-4o
D3-2o
11.D3
12.D3
9.D3
10.D3
D3-3o
D3-2e
D3-1e
7.D3
8.D3
D3
This slide depicts the complete Topology internal to the multi-domain-controller*
It is assumed that the exposed TAPI Context Topology is same as the domain-controller’s internal Context
It is assumed that no Connectivity has been setup in the entire domain and this is the initial Topology view
TAPI Context-3
  *The multi-domain controller may have to invoke more than one retrieval API operation to get this view
D3-3
D3-1
D3-2
D3-4
R-2
R-4
G-2
G-4
10
9
UNI
UNI
11
12
7
Domain-3
8
Physical Box View (internal)
Node Edge Point (Internal)
Service End Point
Node Edge Point (Edge)
Link
Transitional Link
Mapping
Topology
Node
Connection EndPoint
Connection
Connectivity Service
NNI

## Slide 8: Domain-3 TAPI Context Hierarchical Topology (2-Level)
D3-1o
D3-4o
D3-2o
11.D3
12.D3
9.D3
10.D3
D3-3o
D3-2e
D3-1e
D3o
D3e
7.D3
8.D3
D3
This slide depicts complete Topology exposed to multi domain-controller as 2-Level hierarchy*
  It is assumed that the exposed TAPI Context top-level Topology is an 2 Node abstraction of domain-controller‘s internal Context
  This view is constructed by recursively traversing/expanding the internal Topology of top-level Nodes
It is assumed that no Connectivity has been setup in the entire domain and this is the initial Topology view
TAPI Context-3
  *The multi-domain controller may have to invoke more than one retrieval API operation to get this view
D3-3
D3-1
D3-2
D3-4
R-2
R-4
G-2
G-4
10
9
UNI
UNI
11
12
7
Domain-3
8
Physical Box View (internal)
D3e
D3o
Node Edge Point (Internal)
Service End Point
Node Edge Point (Edge)
Link
Transitional Link
Mapping
Topology
Node
Connection EndPoint
Connection
Connectivity Service
NNI

## Slide 9: MD Controller Local Resource Pool (Internal)
D1-o
D1-e
D3-1o
D3-4o
D3-2o
11.D3
12.D3
10.D3
9.D3
D3-3o
D3-2e
D3-1e
7.D3
8.D3
D2-3o
D2-2o
6.D2
5.D2
8.D2
7.D2
D2-1o
D2
D3
1.D1
2.D1
5.D1
6.D1
3.D1
4.D1
D1
MD Controller Internal View (not exposed)
This slide depicts the complete Topology internal to the multi-domain-controller in terms of TAPI-like constructs*
  This view is not exposed to the applications over TAPI.
  The abstraction mapping is maintained internally by the domain controller
It is assumed that no Connectivity has been setup in the entire domain and this is the initial internal Topology view
* An controller internal model may not be based on TAPI
1.G
2.R
3.G
4.R
11.G
12.R
10.G
9.R

## Slide 10: Green TAPI Context Topology (single-layer example)
This slide depicts the complete Topology exposed by the multi-domain-controller to the Green application
It is assumed that the exposed TAPI-Context Topology is a single Node abstraction of the multi-domain-controller ‘s internal Context
It is assumed that this is an ETH layer Topology
  The LayerProtocol of NodeEdgePoints contain attributes specified by the Ethernet extension schema
It is also possible that no layer information is exposed and the layer specific information is implicitly known to the client and provider
It is assumed that no Connectivity has been setup in the entire domain and this is the initial Topology view
  *The application may have to invoke more than one retrieval API operation to get this view
G1.e
1.G
3.G
G
Green TAPI Context
11.G
10.G
Node Edge Point (Internal)
Service End Point
Node Edge Point (Edge)
Link
Transitional Link
Mapping
Topology
Node
Connection EndPoint
Connection
Connectivity Service

## Slide 11: Green TAPI Context Topology (single layer example)
R1.e
This slide depicts an alternate Topology exposed by the multi-domain-controller to the Green application
It is assumed that the exposed TAPI-Context Topology is an edge-Node abstraction of the multi-domain-controller ‘s internal Context
It is assumed that this is an ETH layer Topology
  The LayerProtocol of NodeEdgePoints contain attributes specified by the Ethernet extension schema
It is assumed that no Connectivity has been setup in the entire domain and this is the initial Topology view
  The ETH layer Links are an abstraction of the potential connectivity at this layer
  TAPI Capacity pac is used to represent all the potential, provisioned and available capacity information
  *The application may have to invoke more than one retrieval API operation to get this view
1.G
3.G
G
Green TAPI Context
11.G
10.G
R3.e
R2.e
Node Edge Point (Internal)
Service End Point
Node Edge Point (Edge)
Link
Transitional Link
Mapping
Topology
Node
Connection EndPoint
Connection
Connectivity Service

## Slide 12: Red TAPI Context Topology (multi-layer example)
R3.o
R1.o
R1.e
This slide depicts a multilayer Topology exposed by the multi-domain-controller to the Red application
It is assumed that the exposed TAPI-Context Topology is per-layer-Node abstraction of the multi-domain-controller’s internal Context
It is assumed that this is an ETH + ODU layer Topology
It is assumed that no Connectivity has been setup in the entire domain and this is the initial Topology view
  Initially there no Links in the ETH layer
  The ODU layer Links are an abstraction of the potential connectivity at this layer
  *The application may have to invoke more than one retrieval API operation to get this view
2.R
4.R
R
Red TAPI Context
12.R
9.R
R3.e
R2.o
Node Edge Point (Internal)
Service End Point
Node Edge Point (Edge)
Link
Transitional Link
Mapping
Topology
Node
Connection EndPoint
Connection
Connectivity Service

## Slide 13: Red TAPI Context Topology (multi-layer example)
R3.o
R2.o
R1.o
R1.e
This slide depicts an alternate Topology exposed by the multi-domain-controller to the Red application
It is assumed that the exposed TAPI-Context Topology is an edge-Node abstraction of the multi-domain-controller ‘s internal Context
It is assumed that this is an ETH + ODU layer Topology
It is assumed that no Connectivity has been setup in the entire domain and this is the initial Topology view
  Initially there no Links in the ETH layer
  The ODU layer Links are an abstraction of the potential connectivity at this layer
  *The application may have to invoke more than one retrieval API operation to get this view
2.R
4.R
R
Red TAPI Context
12.R
9.R
R3.e
R2.e
Node Edge Point (Internal)
Service End Point
Node Edge Point (Edge)
Link
Transitional Link
Mapping
Topology
Node
Connection EndPoint
Connection
Connectivity Service

## Slide 14: Service Example 10G EPL
Node Edge Point (Network Internal)
1
Service EndPoint
Node Edge Point (Network Edge)
TAPI Context-1
TAPI Context-R
TAPI Context-G
Domain-1 Controller
Domain-2 Controller
Domain-3 Controller
Multi-Domain Controller
1.D1
2.D1
5.D1
6.D1
TAPI Context-2
5.D2
6.D2
7.D2
8.D2
TAPI Context-3
7.D3
8.D3
11.D3
12.D3
1.G
10.G
2.R
9.R
3.D1
4.D1
9.D3
10.D3
3.G
11.G
4.R
12.R
D1-3
D1-1
D1-2
D1-4
R-1
R-3
G-1
G-3
3
4
UNI
NNI
UNI
NNI
D2-3
D2-1
D2-2
5
6
Domain-1
1
2
D3-3
D3-1
D3-2
D3-4
R-2
R-4
G-2
G-4
10
9
UNI
UNI
11
12
7
8
Domain-3
Domain-2
1
2
3
4
5
13
6
8
7
9
11
10
12

## Slide 15: 10G EPL Service Setup Sequence
Green-app requests 10G EPL ConnectivityService between SEPs (1.G, 11.G)
MD-controller computes & provisions E2E connectivity within its internal topology
MD-controller requests 10G ConnectivityService between SEPs (1.D1, 5.D1)
  Domain1-controller computes & provisions ODU+ETH Connections in its domain
  Domain1-controller returns provisioned Connections in terms of Context-1 topology
MD-controller requests 10G ConnectivityService between SEPs (5.D2, 7.D2)
  Domain2-controller computes & provisions ODU Connections in its domain
  Domain2-controller returns provisioned Connections in terms of Context-2 topology
MD-controller requests 10G ConnectivityService between SEPs (7.D3, 11.D3)
  Domain3-controller computes & provisions ODU+ETH Connections in its domain
  Domain3-controller returns provisioned Connections in terms of Context-3 topology
MD Controller updates its internal Topology and resource pool capacity/usage metrics
MD-controller returns provisioned Connections in terms of Context-G topology
  MD-controller updates capacity/usage metrics in Context-G topology
1
2
3
4
5
6
7
8
9
10
11
12
13
parallel requests

## Slide 16: 10G EPL Service setup: Green Context
R1.e
  *The application may have to invoke more than one retrieval API operation to get this view
3.G
G
Green TAPI Context
10.G
R3.e
R2.e
Node Edge Point (Internal)
Service End Point
Node Edge Point (Edge)
Link
Transitional Link
Mapping
Topology
Node
Connection EndPoint
Connection
Connectivity Service
11.G
1.G
1
13

## Slide 17: 10G EPL Service setup: MD Controller Internal view
D1-e
D1-o
D3-1o
D3-4o
D3-2o
11.D3
12.D3
10.D3
9.D3
D3-3o
D3-2e
D3-1e
7.D3
8.D3
D2-3o
D2-2o
6.D2
5.D2
8.D2
7.D2
D2-1o
D2
D3
2.D1
5.D1
6.D1
3.D1
4.D1
D1
MD Controller Internal View (not exposed)
* An controller internal model may not be based on TAPI
2.R
3.G
4.R
12.R
10.G
9.R
1.G
11.G
1.D1
3
6
8
12
9
2
11
11
12
5
5

## Slide 18: 10G EPL Service setup: DC1/Context1 view
D1-o
D1-e
2.D1
6.D1
3.D1
4.D1
D1
TAPI Context-1
  *The multi-domain controller may have to invoke more than one retrieval API operation to get this view
D1-3
D1-1
D1-2
D1-4
R-1
R-3
G-1
G-3
3
4
UNI
UNI
Domain-1
1
2
Physical Box View (internal)
5
6
Node Edge Point (Internal)
Service End Point
Node Edge Point (Edge)
Link
Transitional Link
Mapping
Topology
Node
Connection EndPoint
Connection
Connectivity Service
NNI
3
5.D1
1.D1
4
5
5

## Slide 19: 10G EPL Service setup: DC2/Context2 view
D2-3o
D2-2o
6.D2
5.D2
8.D2
7.D2
D2-1o
D2
TAPI Context-2
  *The multi-domain controller may have to invoke more than one retrieval API operation to get this view
D2-3
D2-1
D2-2
Physical Box View (internal)
Domain-2
5
6
7
8
Node Edge Point (Internal)
Service End Point
Node Edge Point (Edge)
Link
Transitional Link
Mapping
Topology
Node
Connection EndPoint
Connection
Connectivity Service
NNI
NNI
6
8
7

## Slide 20: 10G EPL Service setup: DC3/Context3 view
D3-1o
D3-4o
D3-2o
11.D3
12.D3
9.D3
10.D3
D3-3o
D3-2e
D3-1e
7.D3
8.D3
D3
TAPI Context-3
  *The multi-domain controller may have to invoke more than one retrieval API operation to get this view
D3-3
D3-1
D3-2
D3-4
R-2
R-4
G-2
G-4
10
9
UNI
UNI
11
12
7
Domain-3
8
Physical Box View (internal)
Node Edge Point (Internal)
Service End Point
Node Edge Point (Edge)
Link
Transitional Link
Mapping
Topology
Node
Connection EndPoint
Connection
Connectivity Service
NNI
9
11
11
10